## Slide 1
DirtBot Electrical Function Overview
24V PSU
22V to 5V Step Down Layer
Arduino MEGA 2560
Motor Controllers
Quad Encoders
Limit Switches
Piezoelectric Micro Blower
Motors
Blower Driver Circuit
Wall Wort 18V PSU
+PWR / +DIR
Digital
Digital
+PUL / +DIR

## Slide 2
DirtBot Software Architecture Overview
main routine:
User input : YAML configuration of tray size and parameters
User feedback: runtime and status output on 16x2 char LCD
Control runtime:
- Startup & calibration sequence
for establishing motor home
- Interprets user config
and generates position instructions
as 2D list of x and y positions
- Step into plug filling routine, each list element runs dispensing
operation and cleans up
– Error monitoring and runtime calculation
Stepper driver
Encoder feedback:
- Accel / decel curve
- Position feedback
Limit switch feedback:
- Interrupts stepper
- Re-establishes home
Environment variables:
- Pin assignment
- User assigned data
- Calibration data
- Stepper, encoder, and LCD objects